## Slide 1: DMAS: Decentralized Multiagent Simulation – System Architecture
Alan Aguilar Jaramillo, Ben Gorr, Chrissi Erwin, Dr Daniel Selva Valero

## Slide 2: Motivation and Challenges
Space-based Earth observation is undergoing a paradigm change
Easier access to space
  More affordable access to space
  Higher grade commercial off-the shelf components
  Increased computation power
Implementation of Distributed Architectures
  Many smaller and heterogeneous satellites, w/ crosslinks
  Federations (coordination among assets owned and operated by different organizations)
  Onboard measurements processing
  Starting to be implemented (e.g., TROPICS [1], CYGNSS [2])
NASA Sensor Web concept (image credit NASA GSFC)
Due to operations logistics, large constellations demand autonomous operations to maximize performance

## Slide 3: Mission Concept: 3D-CHESS
Goal: provide proof of concept for a context-aware network of heterogeneous sensors, in the context of an inland water ecosystem monitoring mission
1 – Default missions; data processing
2 – Event detected; task request sent
3 - Knowledge-based task filtering
4 – Decentralized planning
Proposed 3D-CHESS Scenario
Proposed 3D-CHESS Concept of Operations
Notes: To give you an idea of where we are today in terms of actual missions that have flown

## Slide 4: Mission Concept: 3D-CHESS
Goal: provide proof of concept for a context-aware network of heterogeneous sensors, in the context of an inland water ecosystem monitoring mission
Proposed 3D-CHESS Simulation Framework
Proposed 3D-CHESS Scenario
Notes: To give you an idea of where we are today in terms of actual missions that have flown

## Slide 5: Decentralized Multiagent Simulation (DMAS)
Environment
Server
Agent 3
Client
Agent 1
Client
Agent 2
Client
Agent to Environment: Sense agent state, perform measurement
Environment to all Agents: Broadcasts simulation events
Agent to Agent: Task requests, Information requests, planner results, measurement results
Proposed 3D-CHESS Simulation Framework
DMAS Simulation Framework

## Slide 6: Environment Server Architecture
Simulation Control
Initialize network and wait for all agents to synchronize with the server
Generate and publish a ledger of agent port addresses
Broadcast simulation start and end
Broadcast simulation time (optional)
Earth System Simulator
Propagate the state of the world
Create data for instrument to measure
Agent External State Propagator
Agent position, velocity, attitude, and eclipse state
Respond to requests from agents (be sensed by agents)
Broadcast agent-related events
  i.e., inform agent that it has entered eclipse, so its solar panels stop producing power regardless of whether the agent sensed the eclipse or not.
Environment
Server
Earth System Simulator
Agent External State Propagator
Simulation Control
PUB
REP
-Simulation Control Events
-Simulation Clock (optional)
-Measurement observation metrics req
-Agent Events
Agents
-GP access req
-GS access req
-Agent access req
-Agent state req
Objective: Make the environment house all “True/Real” values of the simulation and have the agents sense those values through their sensors and instruments.

## Slide 7: Agent Simulation Architecture
Proposed 3D-CHESS Agent Framework
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Scheduled Measurement Measurements
-Planner Results (out)
-Measurement Requests
-Estimated measurements’ Science Benefit
-Estimated measurements’ observation metrics
DMAS Agent Framework
-Measurement Requests (out)
-Information Request
-Measurement Results (from self or other agents)
-Agent State
-Planner Results (in)
-Measurement Requests (in)

## Slide 8: Agent Simulation Architecture
Proposed 3D-CHESS Agent Framework
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Scheduled Measurement Measurements
-Planner Results (out)
-Measurement Requests
-Estimated measurements’ Science Benefit
-Estimated measurements’ observation metrics
DMAS Agent Framework
-Measurement Requests (out)
-Information Request
-Measurement Results (from self or other agents)
-Agent State
-Planner Results (in)
-Measurement Requests (in)

## Slide 9: Engineering Module
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Measurement Requests (out)
-Information Request
-Measurement Results (from self or other agents)
-Scheduled Measurement Measurements
-Planner Results (out)
DMAS Agent Framework
-Agent State
-Planner Results (in)
-Measurement Requests (in)
-Measurement Requests
-Estimated measurements’ Science Benefit
-Estimated measurements’ observation metrics
Desired Capabilities:
Agent State Tracking
Sense and track agent’s external state (position, velocity, attitude, and eclipse)
Track agent’s internal state (power and data generation, storage, and consumption, component status, etc.)
React to environment events
  i.e., turn off solar panels if eclipse event occurs
Scheduler Action Performance and Rejection
Receive and perform instructions from scheduler
Revert actions or even turn off agent if a critical state is reached
  i.e., interrupt a measurement if power consumption from instruments exceeds generation
Instrument Simulation
Sense the environment
Provide realistic measurement results to science module
Network Simulator
Send and receive messages from/to other agents
Capture network delays
  Due to transmission latency and data-rate
  Due to buffer saturation
Objective: Simulate the agent’s internal state and provide realistic behavior and capabilities based on its components and operations

## Slide 10: Engineering Module
Agent
Environment
Other Agents
SUB
REQ
REP
REQ
Engineering Module
Science Module
Planning Module
-Environment Events
-Simulation Events
-GP access
-Agent access
-Agent position, vel
-Agent eclipse
-GP measurement observation metrics
-Measurement Request (out)
-Information Request (out)
-Measurement Results (out)
-Planner Results (out)
-Measurement Request (in)
-Information Request (in)
-Measurement Results (in)
-Planner Results (in)
Event Handler
Sim Start/End
Simulation Maintenance Module
-Simulation Events
-Measurement Request (out)
-Information Request (in/out)
-Planner Results
-Measurement Requests (in)
-Measurement Requests
-Estimated measurements’ science benefit
-Estimated measurements’ observation metrics
Network Sim
Platform Sim
Operations Executor
Instrument Simulator
-Measurement Request (in/out)
-Information Request (in/out)
-Measurement Results (in/out)
-Planner Results (in/out)
-GP access req
-GP measurement observation metrics req
-Agent access
-Environment Events
-Environment Events
-Agent State Events
-Agent State
-Component Actuation Actions
-Measurement Actions
-Scheduled Measurement Actions
-Measurement Results (from self)
-Agent State
Knowledge-Base and Predictive Models
-Agent position, vel
-Agent eclipse
-Agent State
-Next predicted critical state
-Agent component capabilities

## Slide 11: Engineering Module - Plan Execution
Plan Execution Sequence:
Scheduler Module
Platform Sim
Operations Planner
“Perform measurement of GP 123 @ t=5 w/ instr1”
Receive measurement plan from scheduler
Plan Execution Sequence:
Scheduler Module
Platform Sim
Operations Planner
1- Wait for t = 5
2- Maneuver to observe GP 123 with instr1
3- Turn on instr1
4- Sense GP 123
5- Turn off intr1
Generate operations plan from measurement plan
Plan Execution Sequence:
Scheduler Module
Platform Sim
Operations Planner
“Waiting for t=5…
Wait complete!
State is nominal, proceed to next instruction”
Execute Plan
Plan Execution Sequence:
Scheduler Module
Platform Sim
Operations Planner
“cancel plan”
React to Plan Execution Errors
“Performing maneuver…
Power insufficient to perform maneuver. Cancelling action and reassessing plan…”

## Slide 12: Agent Simulation Architecture
Proposed 3D-CHESS Agent Framework
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Scheduled Measurement Measurements
-Planner Results (out)
-Measurement Requests
-Estimated measurements’ Science Benefit
-Estimated measurements’ observation metrics
DMAS Agent Framework
-Measurement Requests (out)
-Information Request
-Measurement Results (from self or other agents)
-Agent State
-Planner Results (in)
-Measurement Requests (in)

## Slide 13: Agent Simulation Architecture
Proposed 3D-CHESS Agent Framework
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Scheduled Measurement Measurements
-Planner Results (out)
DMAS Agent Framework
-Measurement Requests (out)
-Information Request
-Measurement Results (from self or other agents)
-Agent State
-Planner Results (in)
-Measurement Requests (in)
-Measurement Requests
-Estimated measurements’ Science Benefit
-Estimated measurements’ observation metrics

## Slide 14: Science Module
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Scheduled Measurement Measurements
-Planner Results (out)
DMAS Agent Framework
-Measurement Requests (out)
-Information Request
-Measurement Results (from self or other agents)
-Agent State
-Planner Results (in)
-Measurement Requests (in)
-Measurement Requests
-Estimated measurements’ Science Benefit
-Estimated measurements’ observation metrics
Desired Capabilities:
On-board Data Processing
Process raw data being sensed by the agent’s instrument
Process raw data sent from other agents who may lack processing capabilities
Create measurement requests for areas of interest
Create a data-base with measurements from parent agent or from other agents
Use data-base to detect areas of interest based on processed data
Use predictive models to infer possible future events in areas of interest
Request missing data as a measurement request or an information request to parent agent or to other agents if results would complete predictive model and if prediction would be worth the effort
Quantify Scientific Value of a Measurement
Use predictive models, data-base, and (or) mission requirements to infer the scientific benefit of a potential measurement being considered by the scheduler
Objective: Simulate the agent’s internal state and provide realistic behavior and capabilities based on its components and operations

## Slide 15: Science Module
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Scheduler Module
Science Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Measurement Results (from self or other agents)
-Agent State
-Planner Results (in)
-Scheduled Measurement Measurements
-Planner Results (out)
On-board Processor
Science Value Model
Science Predictive Models
-Measurement Requests
-Estimated measurements’ observation metrics
Science data-base
-Estimated measurements’ Science Benefit
-Measurement Requests
-Information Request
-Measurement Results (from self)
-Mission Requirements
-Past measurement data
Science “reasoning”
-Processed data
-Model req/results
-Model req/results
-Past data

## Slide 16: Science Module – Chl example
Agent
Science Module
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Scheduler Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Raw multi/hyperspectral images (from self or other agents)
-Agent State
-Planner Results (in)
-Scheduled Measurement Measurements
-Planner Results (out)
On-board Processor – 2BDA algorithm
Science Value Model
Science Predictive Models – rainfall? Temperature? Historical?
-Measurement Requests
-Estimated measurements’ observation metrics
Science data-base – past and current chlorophyll levels
-Estimated measurements’ Science Benefit
-Measurement Requests
-Information Request
-Measurement Results (from self)
-Mission Requirements
-Past measurement data
Science “reasoning” – sees if chlorophyll concentration is above 1 standard deviation
-Chl-a product
-Past chl-a levels
-Observation metrics
-Algal bloom likelihood
-Chl-a outliers

## Slide 17: Agent Simulation Architecture
Proposed 3D-CHESS Agent Framework
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Scheduled Measurement Measurements
-Planner Results (out)
-Measurement Requests
-Estimated measurements’ Science Benefit
-Estimated measurements’ observation metrics
DMAS Agent Framework
-Measurement Requests (out)
-Information Request
-Measurement Results (from self or other agents)
-Agent State
-Planner Results (in)
-Measurement Requests (in)

## Slide 18: Agent Simulation Architecture
Proposed 3D-CHESS Agent Framework
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Scheduled Measurement Measurements
-Planner Results (out)
DMAS Agent Framework
-Measurement Requests
-Estimated measurements’ Science Benefit
-Estimated measurements’ observation metrics
-Measurement Requests (out)
-Information Request
-Measurement Results (from self or other agents)
-Agent State
-Planner Results (in)
-Measurement Requests (in)

## Slide 19: Scheduler Module
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Scheduled Measurement Measurements
-Planner Results (out)
DMAS Agent Framework
-Measurement Requests
-Estimated measurements’ Science Benefit
-Estimated measurements’ observation metrics
-Measurement Requests (out)
-Information Request
-Measurement Results (from self or other agents)
-Agent State
-Planner Results (in)
-Measurement Requests (in)
Desired Capabilities:
Consider Agent capabilities
Use Knowledge-Base to inform whether the agent can perform a measurement
Consider agent’s current and future state
Use engineering module for current state
Predict agent state as proposed scheduled actions are being performed
Schedule measurements as to maximize scientific value and minimize cost
Quantify the predicted scientific value of a measurement and schedule accordingly
Contain some sort of cost model that weighs down the value of measurements. Can be tied to the engineering cost of performing measurements
Publish and receive results to and from other agent if scheduling algorithm require collaboration with other agents
Objective: Schedule measurement requests according to the agent’s measurement capabilities and state

## Slide 20: Scheduler Module
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler/Planning Module
-Environment Events
-Simulation Events
-GP access req
-GS access req
-Agent access req
-Agent state req
-Measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Environment Events
-Measurement Requests (out)
-Information Request
-Measurement Results (from self or other agents)
-Agent State
-Planner Results
-Scheduled Measurement Measurements
-Planner Results (out)
-Proposed measurements’ estimated Science Benefit
-Estimated measurements observation metrics
Decentralized Observation Planning (multi-agent level)
Predictive Models
Knowledge-Base Instrument Capability Reasoning
-Proposed measurements
-Planner Results
-Estimated measurements observation metrics
-Other agents’ capabilities
-Proposed measurements
-Measurement Requests
-Measurement Requests (in)
Cost Models
-Agent State
-Proposed Plan
-Plan Cost Estimate
DL/ISL/Maneuver (Ops) Scheduling Algorithm (agent level)
Science Models

## Slide 21: Agent Simulation Architecture
Module
Properties
Queue inbox
Module* parentModule
Array<Module*> submodules
Methods
void internal_message_router()
void internal_message_handler()
void routine()
Agent Client
Properties
Port environment_broadcast
Port environment_request
Port agent_request
Port agent_responce
Methods
void broadcast_handler()
void submit_request()
Environment Server
Properties
Port reqservice
Port publisher
Methods
void broadcast_handler()
void request_handler()
Environment
Server
Agent 3
Client
Agent 1
Client
Agent 2
Client
Agent to Environment: Sense agent state, perform measurement
Environment to all Agents: Broadcasts simulation events
Agent to Agent: Task requests, Information requests, planner results, measurement results
DMAS Simulation Framework

## Slide 22: Development Status
Simulation Architecture
Environment Server
Spacecraft agent orbit data propagator (orbitPy)
Agent state request handler
Agent eclipse broadcast
Simulation start/end broadcast
Measurement request handler
Earth simulation module
Agent
Environment broadcast handler
Environment request submitter
  State request
  Eclipse request
  Ground station access request
  Ground point access request
  Ground point measurement request
Agent-to-agent request handler
Agent-to-agent response handler
Github (private repo for now)
Modules
Engineering Module
Define system architecture
Platform Simulator
  Power Tracking
  Data Tracking
  Shutdown if critical
Network Simulator
Instrument Simulator
  Develop tool (instruPy)
  Implement tool
Operations Planner
  Develop rules
  Implement rules
Knowledge-base and Predictive models
  Develop rules
  Implement Rules
Scheduling Module
Define system architecture
Begin development
Science Module
Define system architecture
Begin development

## Slide 23: Questions?

## Slide 24: References
WJ, Blackwell, Braun, S, Bennartz, R, et al. An overview of the TROPICS NASA Earth Venture Mission. Q J R Meteorol Soc. 2018; 144 ( Suppl. 1): 16– 26
M. P. Clarizia and C. S. Ruf, "Wind Speed Retrieval Algorithm for the Cyclone Global Navigation Satellite System (CYGNSS) Mission," in IEEE Transactions on Geoscience and Remote Sensing, vol. 54, no. 8, pp. 4419-4432, Aug. 2016, doi: 10.1109/TGRS.2016.2541343.
Marinan, A., Cahoy, K. L., Byrne, J., Cordeiro, T., Decker, Z., Marlow, W., ... & Osaretin, I. (2015). Automated Resource-Constrained Science Planning for the MiRaTA Mission.
W. J. W. J. Wolfe and S. E. S. E. Sorensen, “Three Scheduling Algorithms Applied to the Earth Observing Systems Domain,” Manage. Sci., pp. 148–166, 2000.
Duncan, Eddy, and Kochenderfer, Mykel. “Markov Decision Processes For Multi-Objective Satellite Task Planning”,
Cidoncha, X. G., and Selva, D., “Agent-based simulation framework and consensus algorithm for observing systems withadaptive modularity,”Syst. Eng., Vol. 21, no. 5, 2018, pp. 432–545.
Nag, Sreeja, et al. "Autonomous scheduling of agile spacecraft constellations with delay tolerant networking for reactive imaging." (2019).
H. Wang, X. Li, and Y. Liu, “Summary of intelligent algorithms in planning & amp; scheduling of Earth observation satellite,” in IEEE International Conference on Intelligent Computing and Intelligent Systems, 2010, pp. 480–483.
Kennedy, Andrew K., and Kerri L. Cahoy. "Performance analysis of algorithms for coordination of earth observation by cubesat constellations." Journal of Aerospace Information Systems 14.8 (2017): 451-471.
Li, G. 2020. Online scheduling of distributed Earth observation satellite system under rigid communication constraints. Advances in Space Research. 65 (11), 2475-2496.
Gallud,X.,andSelva,D.,“Agent-basedsimulationframeworkandconsensusalgorithmforobservingsystemswithadaptive modularity,” Syst. Eng., 2018, pp. 432, 454.
S. Nag et al., "D-SHIELD: DISTRIBUTED SPACECRAFT WITH HEURISTIC INTELLIGENCE TO ENABLE LOGISTICAL DECISIONS," IGARSS 2020 - 2020 IEEE International Geoscience and Remote Sensing Symposium, 2020, pp. 3841-3844, doi: 10.1109/IGARSS39084.2020.9323248.

## Slide 25: Backup Slides

## Slide 26: Decentralized Multiagent Simulation (DMAS)
Environment Server
Simulate State of the Earth
Respond to information requests from Agents
  Agent position, velocity, eclipse state
  Current agents, ground points, or ground stations being accessed by Agents
  Measurement Information
Broadcast Environment Events to all Agents
  Simulation Start/End
  Agent enters/exits eclipse
  Simulation clock (optional)
Agent Client
Track and affect internal state
  Power and data usage, generation, and storage
  Actuating components on or off
  Performing Maneuvers
  Charging Batteries
Communicate with other agents
  Measurement or Information Task Requests
  Measurement or Planner Results
Affect Environment
  Communicating maneuvers to Environment
Environment
Server
Agent 3
Client
Agent 1
Client
Agent 2
Client
Agent to Environment: Sense agent state, perform measurement
Environment to all Agents: Broadcasts simulation events
Agent to Agent: Task requests, Information requests, planner results, measurement results
DMAS Simulation Framework

## Slide 27: Simulation Framework
Agent
Environment
Other Agents
SUB
REQ
REP
REQ
Engineering Module
Science Module
Science Scheduler
-Environment Events
-Simulation Events
-GP access req
-Agent access req
-Agent position req
-Agent eclipse req
-GP measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Maintenance Module
-Simulation Events
-Environment Events
-Measurement Requests
-Information Request
-Measurement Results (from self or other agents)
-Agent State
-Planner Results (in)
-Scheduled Measurement Measurements
-Planner Results (out)
-Measurement Requests
-Proposed measurements’ estimated Science Benefit
-Proposed measurements
-Proposed measurements’ estimated observation metrics
Nomenclature:
Communications Port
Agent Module/Submodule
Process
Inter-process/module
communication link
Inter-agent
communication link
Process Sequence
SUB
Module
Sim Start/End
Proposed 3D-CHESS Agent Framework
DMAS Agent Framework

## Slide 28: Requirement-Driven Utility Function
Desired Dependencies
Temporal Constraints
  Cross-registration with other satellites
Urgency
  e.g., short-lived phenomena
Stakeholder Requirement Satisfaction
  Spatial Resolution, Measurement Accuracy, etc…
Maneuvering Costs
Measurement Intrinsic Costs
: Measurement task j
: Time of Measurement of Task j
: Maximum Score
: Level of Completion of Task j
: Weight of Requirement i
: Urgency Factor
: Reference performance metric
: Estimated performance
: Urgency Factor
: Task start time

## Slide 29: Simulation Framework
Agent
Environment
Other Agents
SUB
REQ
REP
REQ
Engineering Module
-Environment Events
-Simulation Events
-GP access req
-Agent access req
-Agent position req
-Agent eclipse req
-GP measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Maintenance Module
-Simulation Events
Network Sim
send_transmission():
---------------------------------------------------------------
Receive Transmission Request
Await self buffer allocation
Create Routing Plan
Await Access Start
Establish link
Await receiver’s buffer allocation
Start transmission
Await transmission completion
Simulate remaining time Delay
Delete message from buffer
receive_transmission():
---------------------------------------------------------------
Await reception request
Await to allocate transmission in buffer
Send allocation confirmation
Await transmission completion
Simulate remaining time delay
Delete message from buffer
Send transmission message to destined module for processing

## Slide 30: Simulation Framework
Agent
Environment
Other Agents
SUB
REQ
REP
REQ
Engineering Module
-Environment Events
-Simulation Events
-GP access req
-Agent access req
-Agent position req
-Agent eclipse req
-GP measurement observation metrics req
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
-Measurement Request
-Information Request
-Measurement Results
-Planner Results
Event Handler
Sim Start/End
Simulation Maintenance Module
-Simulation Events
Platform Sim
Internal_message_handler():
---------------------------------------------------------------
Await message
If message not meant for this module, forward to destination
If environment event, update state
If maintenance action, perform measurement
If measurement action,
If buffer allocation action,
If state request, send latest state
If critical state flag, request actions to operations planner. If no response and still critical, set platform state to false, else do actions and exit process
perform_measurement():
---------------------------------------------------------------
asd
periodic_update():
---------------------------------------------------------------
Wait 1 time-step
Update state
Repeat forever
update_state():
---------------------------------------------------------------
dt = current time – previous update time
Update power and data for dt
Check if in eclipse
Check for pos and vel
Update component status
Trigger updated event
critical_state_timer():
---------------------------------------------------------------
Get current state
If critical, send critical state flag and return
Predict next critical state
Await next critical state or updated event
If updated event, repeat from 1
Else, send critical state flag
run():
---------------------------------------------------------------
Wait for all to end: internal_message_handler(), critical_state_timer()

## Slide 31: ToDo’s
Engineering Model Integration
Alan: Power and Data Tracking Model
Ben: Attitude Model
Science Value Module
Ben: Spatial Res + Look Angle-based Chlorophyll + TSS
Federated Systems
Define federation in simpy
Use Case
Define federation in simpy

## Slide 32: Types of Requests
Past Information Request
  “I want soil moisture at (X,Y), does anyone know about this?”
  “I am measuring SM at (X,Y) in 5 mins but need temperature measurements, does anyone know about this recently?”
  “I an optical measurement from (X,Y), can you tell me if there is Algae here?”
New/Future Measurement Request
  “Can someone measure SM at (X,Y) and tell me what the value is?”
Force Measurement Request
  “You are measuring SM at (X,Y) because we told you to.”
Publish and subscribe protocol?
Sat X performs periodic measurements and list of Sats X_i receive the periodical data
Request protocol?
Only request the information you need

## Slide 33: End Users
Initial Focus: Data collection of the network
Later Focus: Data downlink and information quality
  Use case-specific metrics
    i.e., How many times were algae blooms detected in single sat mission vs distributed mission
  Evaluated information is obtained from GS performing information requests

## Slide 34: Validation
Value of context-awareness
  Fixed plan vs reactive plan
  Importance of different information
    No state info, no information requests